## Slide 1: Introduction to NMAP

## Slide 2: Need for NMAP
Identifying open ports
Network Mapping
Auditing security

## Slide 3: NMAP
Developed by Gordon Lyon
Features
  Host discovery
  Port scanning
  Version detection
  OS detection
  Scriptable interaction with the target

## Slide 4: Environment & GUI
Runs on Linux, Windows, Mac OS X and other smaller operating systems
GUI options:
  Zenmap
  XNMap
  NmapFE

## Slide 5: Port scanning

## Slide 6: How NMAP Works
NMap pings the remote target with 0 byte packets to each port
  If packets are not received back, port is open
  If packets are received, port is closed
Sends different packets with different timing to determine filtered/unfiltered, version, etc.
Firewalls can interfere with this process

## Slide 7: If port is Open
NMAP performs the scan by sending a SYN packet and look for the response. If SYN/ACK is received, the port is open.
The scanner then sends an RST to tear down the connection before it can be established fully

## Slide 8: If port is Closed
If the port is closed, an RST will be sent.
If port is Filtered
If it is filtered, the SYN packet will have been dropped and no response will be sent

## Slide 9: Ethical Issues
Can be used for hacking to discover vulnerable ports
System admins can use it to check that systems meet security standards
Unauthorized use of Nmap on a system could be illegal. Make sure you have permission before using this tool

## Slide 10: NMAP work to solve
Find the system and services on the network
Discover information about these systems
Reliable tool for system admin, security professional and hobbyists
Accurate results in scanning

## Slide 11: NMAP – Legal considerations in performing scanning
Is network scanning legal?
  It depends
    Legal if you scan your own network with explicit permission
    Illegal if you scan without any permission

## Slide 12: Laws by country
Differ from country to country
Safety bet is to scan the system which own with prior permission
Think about the target which you want to perform scanning
Can be considered as illegal and it depends on how you use them?

## Slide 13: Network Port
Interface to the application available to the network
Represented by the number
  Web servers – TCP (80/443)
  Email servers – TCP (25,110,143 etc.,)
    DNS servers – UDP (53)

## Slide 14: TCP 3 way handshake
SYN
SYN+ACK
ACK

## Slide 15: List of Scans in NMAP
Intense scan -Should be reasonable quick, scan the most common TCP ports, OS, Services and Versions
Intense scan plus UDP- Same as the regular Intense scan, also scan UDP ports
Intense scan, all TCP ports-Normally Nmap scans a list of 1000 most common protocols, but instead we will in this example scan everything from port 1 to 65535 (max).

## Slide 16: List of Scans
Intense scan, no ping – Similar to other intense scans, however this will assume the host is up. Useful if the target is blocking ping request and you already know the target is up.
Ping scan- Do only a ping only on the target, no port scan.
Quick scan- Scan faster than the intense scan by limiting the number of top 100 TCP ports.

## Slide 17: List of Scans
Quick scan plus –Widely used for OS detection and you got the Quick scan plus.
Quick traceroute – Used to determine hosts and routers in a network scan
Regular scan - Default everything. ICMP Echo request (ping) for host detection. Scans 1000 TCP ports
Slow comprehensive scan – Similar to intense scan plus UDP. It uses all the three protocols to detect the hosts, TCP, UDP and SCTP

## Slide 18: Host discovery
Nmap –sP 192.168.108.1/24
Wireshark
  Sniff on eth0
  Ip.addr==192.168.108.1

## Slide 19: Zenmap – A GUI of NMAP

## Slide 20: OS detection

## Slide 21: Exercises
Identify Which hosts are up now? Apply ping sweeping
    nmap -sn 10.0.0.1/24
Use the TCP "ping" option with a ping scan with a flag to target port
    nmap -sn -PA80 10.0.0.0/24
To scan all the TCP ports
  nmap -p 1-65535 192.168.108.1

## Slide 22: Results Port Sweeping

## Slide 23: ping scan at port 80

## Slide 24: Ping sweep
nmap –sP –oG ping-sweep 192.168.108.1
nmap -sP -oN sibi 192.168.108.1/24

## Slide 25: Saving in xml file
Nmap –oX xml-dump 192.168.108.1

## Slide 26: Reason flag in your scan
nmap -sU --reason 172.168.89.191

## Slide 27: Find out if a host/network is protected by a firewall
nmap -sA 172.168.1.254

## Slide 28: Scan a host when protected by the firewall
nmap -PN 172.168.1.1

## Slide 29: Scan a firewall for security weakness
nmap -sN 172.168.1.254 //No flag bits are set
nmap -sF 172.168.1.254 // sets FIN flag
nmap -sX 172.168.1.254 //sets FIN, PSH, URG

## Slide 30: Cloak a scan with decoys
nmap -n -Ddecoy-ip1,decoy-ip2,your-own-ip,decoy-ip3,decoy-ip4 remote-host-ip
nmap -n -D192.168.1.5,10.5.1.2,172.1.2.4,3.4.2.1 192.168.1.5

## Slide 31: Firewall bypass (locally)
Scan  MAC address spoofing
nmap --spoof-mac MAC-ADDRESS-HERE 172.168.1.1
nmap -v -sT -PN --spoof-mac MAC-ADDRESS-HERE 172.168.1.1
nmap -v -sT -PN --spoof-mac 0 172.168.1.1

## Slide 32: Firewall bypass
nmap -sS -P0 172.168.89.191

## Slide 33: Firewall bypass
nmap --script firewall-bypass --script-args firewall-bypass.helper="ftp", firewall-bypass.targetport=22 172.18.232.1
nmap --script firewall-bypass 172.18.232.1

## Slide 34: Version info
nmap -V 172.168.89.191

## Slide 35: Shodan-api key
nmap --script shodan-api x.y.z.0/24 -sn -Pn -n --script-args 'shodan-api.apikey=SHODANAPIKEY'
nmap --script shodan-api x.y.z.0/24 -sn -Pn -n --script-args 'shodan-api.apikey= <key>'

## Slide 36: virustotal
nmap --script http-virustotal --script-args='http-virustotal.apikey="<key>",http-virustotal.checksum="275a021bbfb6489e54d471899f7db9d1663fc695ec2fe2a2c4538aabf651fd0f"'

## Slide 37: Checks if a web server is vulnerable to directory traversal by attempting to retrieve /etc/passwd or \boot.ini.
nmap --script http-passwd --script-args http-passwd.root=/test/ <target>

## Slide 38: Tests a web server for vulnerability to the Slowloris DoS attack by launching a Slowloris attack.
nmap --script http-slowloris --max-parallelism 400 <target>

## Slide 39: Google safe browsing api
nmap –p80 --script http-google-malware --script-args http-google-malware.api=<api> target

## Slide 40: Grep (ing) public emails using nmap
nmap -p <Port> --script http-grep <target>
nmap –p443 --script http-grep <target>

## Slide 41: Discovering hostnames pointing to the same IP address
nmap -sn --script hostmap-* <target>

## Slide 42: Discovering hostnames by brute forcing DNS records
nmap --script dns-brute –p80 172.18.232.10
nmap --script dns-brute --script-args dns-brute.domain=foo.com,dns-brute.threads=6,dns-brute.hostlist=./hostfile.txt,newtargets -sS -p80 172.18.232.10

## Slide 43: Validate your network broadcast
nmap --script broadcast-listener -e eth0

## Slide 44
In the LAN, how many hosts are running? Please list their IP addresses.
If a computer is up, which services (TCP and UDP) are open on it?
Can you determine the Operating system and its possible version that is running on each alive computer?
Lab Questions

## Slide 45: NMAP Scripting Engine
To perform more complex checks
To infer more information
To allow for greater flexibility

## Slide 46: NSE
The basic structure of an NSE script
Required components of an NSE script
Useful libraries
Portrules

## Slide 47: NSE Structure
The Head
The Rule
The Action

## Slide 48: Script Categories
Auth
Broadcast
Brute
Default
Discovery
DoS
Exploit
Intrusive
Malware
Safe
Version
Vuln

## Slide 49: NSE Libraries
128 NSE libraries built into NMAP
  Nmap
  Nsedebug
  Shortport
  Smb
  Vulns
  ……..

## Slide 50: Importing Libraries
Head Section
  Local shortport = require “shortport”
  Local http = require “http”
  Local stdnse = require “stdnse”

## Slide 51: Building portrules
Portrule = function (host,port)
  Local auth_port = {number =113, protocol =“tcp”}
  Local identd = nmap.get_port_state(host,auth_port)
  Return identd~=Nil and identd.state == “open” and port.protocol == “tcp” and port.state == “open”
  End

## Slide 52: Port rules simplified
--Head
  Local shortport = require “shortport”
  --Rule
  Portrule = shortport.http

## Slide 53: Windows Service Identification
nmap -PS445 -p445 --script=smb-os-discovery,smbv2-enabled,smb-enum-shares,smb-ls --script-args=ls.maxdepth=10 192.168.108.99

## Slide 54: Heart bleed Vulnerability
nmap -d sC --script ssl-heartbleed.nse www.mitindia.edu

## Slide 55: Win32 Services
nmap -d sC --script snmp-win32-services.nse 192.168.108.99

## Slide 56: WCRY - SMB vuln
nmap –d -sC -p 445 --script smb-vuln-ms17-010.nse 192.168.108.99